## Slide 1
Physical Storage Systems
— Chapter 12
叶文
yewen@bupt.edu.cn
School of Computer Science (National Pilot Software Engineering School)
2021年11月

## Slide 2: Outline
Storage Hierarchy
Storage Interfaces
Magnetic Disk
Flash Storage
RAID
Disk-block Access

## Slide 3: 12.1 Classification of Physical Storage Media
Can differentiate storage into:
  volatile storage: loses contents when power is switched off
  non-volatile storage:
    Contents persist even when power is switched off.
    Includes secondary and tertiary storage, as well as batter-backed up main-memory.
Factors affecting choice of storage media include
  Speed with which data can be accessed
  Cost per unit of data
  Reliability

## Slide 4
Fig.12.1 Storage-device hierarchy
Performance Indicators :
CPU
secondary
storage
slow
fast
Speed
Capacity
large
small
low
high
Cost
Reliability
volatile
nonvolatile
tertiary
storage
Storage

## Slide 5: Storage Hierarchy
primary storage: Fastest media but volatile (cache, main memory).
secondary storage: next level in hierarchy, non-volatile, moderately fast access time
  Also called on-line storage
  E.g., flash memory, magnetic disks
tertiary storage: lowest level in hierarchy, non-volatile, slow access time
  also called off-line storage and used for archival storage
  e.g., magnetic tape, optical storage
  Magnetic tape
    Sequential access, 1 to 12 TB capacity
    A few drives with many tapes
    Juke boxes with petabytes (1000’s of TB) of storage

## Slide 6: 12.2 Storage Interfaces
Disk interface standards families
  SATA (Serial ATA)
    SATA 3 supports data transfer speeds of up to 6 gigabits/sec
  SAS (Serial Attached SCSI)
    SAS Version 3 supports 12 gigabits/sec
  NVMe (Non-Volatile Memory Express) interface
    Works with PCIe connectors to support lower latency and higher transfer rates
    Supports data transfer rates of up to 24 gigabits/sec
Disks usually connected directly to computer system
In Storage Area Networks (SAN), a large number of disks are connected by a high-speed network to a number of servers
In Network Attached Storage (NAS) networked storage provides a file system interface using networked file system protocol, instead of providing a disk system interface

## Slide 7: 12.3 Magnetic Disks
Read-write head
Surface of platter divided into circular tracks
  Over 50K-100K tracks per platter on typical hard disks
Each track is divided into sectors.
  A sector is the smallest unit of data that can be read or written.
  Sector size typically 512 bytes
  Typical sectors per track: 500 to 1000 (on inner tracks) to 1000 to 2000 (on outer tracks)
To read/write a sector
  disk arm swings to position head on right track
  platter spins continually; data is read/written as sector passes under head
Head-disk assemblies
  multiple disk platters on a single spindle (1 to 5 usually)
  one head per platter, mounted on a common arm.
Cylinder i consists of ith track of all the platters

## Slide 8: Magnetic Hard Disk Mechanism
Schematic diagram of magnetic disk drive
Photo of magnetic disk drive

## Slide 9
知乎：
为什么硬盘转速是3600、5400或7200这么奇怪的数字？7200转的硬盘一定比5400快吗？
5400转/分钟
=5400 RPM
美国交流电60Hz
1分钟=60秒
60Hz *1转/Hz * 60秒/分钟=3600转/分钟
5400 RPM=1.5*3600RPM
7200 RPM=2*3600RPM

## Slide 10: Magnetic Disks (Cont.)
Disk controller – interfaces between the computer system and the disk drive hardware.
  accepts high-level commands to read or write a sector
  initiates actions such as moving the disk arm to the right track and actually reading or writing the data
  Computes and attaches checksums to each sector to verify that data is read back correctly
    If data is corrupted, with very high probability stored checksum won’t match recomputed checksum
  Ensures successful writing by reading back sector after writing it
  Performs remapping of bad sectors

## Slide 11: Magnetic Hard Disk Mechanism
on-board cache: set of blocks
track
外部传输速率
内部传输速率
disk drive
block-based
Chunk/cluster-based

## Slide 12: Performance Measures of Disks
Access time – the time it takes from when a read or write request is issued to when data transfer begins. Consists of:
  Seek time – time it takes to reposition the arm over the correct track.
    Average seek time is 1/2 the worst case seek time.
      Would be 1/3 if all tracks had the same number of sectors, and we ignore the time to start and stop arm movement
    4 to 10 milliseconds on typical disks
  Rotational latency – time it takes for the sector to be accessed to appear under the head.
    4 to 11 milliseconds on typical disks (5400 to 15000 r.p.m.)
    Average latency is 1/2 of the above latency.
  Overall latency is 5 to 20 msec depending on disk model
Data-transfer rate – the rate at which data can be retrieved from or stored to the disk.
  25 to 200 MB per second max rate, lower for inner tracks

## Slide 13
Operating System Concepts - Chapter12 Mass Storage Structures -
Segate(希捷) SV35 Series ——面向视频监控的高性能、大容量硬盘
硬盘和内存
间cache/buffer
平均寻道
时间 8.5ms
内部传输速率
外部传输速率

## Slide 14: Performance Measures (Cont.)
Disk block is a logical unit for storage allocation and retrieval
  4 to 16 kilobytes typically
    Smaller blocks: more transfers from disk
    Larger blocks: more space wasted due to partially filled blocks
Sequential access pattern
  Successive requests are for successive disk blocks
  Disk seek required only for first block
Random access pattern
  Successive requests are for blocks that can be anywhere on disk
  Each access requires a seek
  Transfer rates are low since a lot of time is wasted in seeks
I/O operations per second (IOPS)
  Number of random block reads that a disk can support per second
  50 to 200 IOPS on current generation magnetic disks

## Slide 15: Performance Measures (Cont.)
Mean time to failure (MTTF) – the average time the disk is expected to run continuously without any failure.
  Typically 3 to 5 years
  Probability of failure of new disks is quite low, corresponding to a “theoretical MTTF” of 500,000 to 1,200,000 hours for a new disk
    E.g., an MTTF of 1,200,000 hours for a new disk means that given 1000 relatively new disks, on an average one will fail every 1200 hours
  MTTF decreases as disk ages

## Slide 16: 12.4 Flash Storage
NOR flash vs NAND flash
NAND flash
  used widely for storage, cheaper than NOR flash
  requires page-at-a-time read (page: 512 bytes to 4 KB)
    20 to 100 microseconds for a page read
    Not much difference between sequential and random read
  Page can only be written once
    Must be erased to allow rewrite
Solid state disks SSD
  Use standard block-oriented disk interfaces, but store data on multiple flash storage devices internally
  Transfer rate of up to 500 MB/sec using SATA, and up to 3 GB/sec using NVMe PCIe

## Slide 17: 面向SSD的新型硬盘接口
mSATA
M.2
PCIE
(直连CPU)

## Slide 18: Flash Storage (Cont.)
Erase happens in units of erase block
  Takes 2 to 5 millisecs
  Erase block typically 256 KB to 1 MB (128 to 256 pages)
Remapping of logical page addresses to physical page addresses avoids waiting for erase
Flash translation table tracks mapping
  also stored in a label field of flash page
  remapping carried out by flash translation layer
After 100,000 to 1,000,000 erases, erase block becomes unreliable and cannot be used
  wear leveling

## Slide 19: SSD Performance Metrics
Random reads/writes per second
  Typical 4 KB reads: 10,000 reads per second (10,000 IOPS)
  Typical 4KB writes: 40,000 IOPS
  SSDs support parallel reads
    Typical 4KB reads:
      100,000 IOPS with 32 requests in parallel (QD-32) on SATA
      350,000 IOPS with QD-32 on NVMe PCIe
    Typical 4KB writes:
      100,000 IOPS with QD-32, even higher on some models
Data transfer rate for sequential reads/writes
  400 MB/sec for SATA3, 2 to 3 GB/sec using NVMe PCIe
Hybrid disks: combine small amount of flash cache with larger magnetic disk

## Slide 20: Storage Class Memory
3D-XPoint memory technology pioneered by Intel
Available as Intel Optane
  SSD interface shipped from 2017
    Allows lower latency than flash SSDs
  Non-volatile memory interface announced in 2018
    Supports direct access to words, at speeds comparable to main-memory speeds

## Slide 21: 12.5 RAID
RAID: Redundant Arrays of Independent Disks
  disk organization techniques that manage a large numbers of disks, providing a view of a single disk of
    high capacity and high speed by using multiple disks in parallel,
    high reliability by storing data redundantly, so that data can be recovered even if a disk fails
The chance that some disk out of a set of N disks will fail is much higher than the chance that a specific single disk will fail.
  E.g., a system with 100 disks, each with MTTF of 100,000 hours (approx. 11 years), will have a system MTTF of 1000 hours (approx. 41 days)
  Techniques for using redundancy to avoid data loss are critical with large numbers of disks

## Slide 22: Improvement of Reliability via Redundancy
Redundancy – store extra information that can be used to rebuild information lost in a disk failure
E.g., Mirroring (or shadowing)
  Duplicate every disk. Logical disk consists of two physical disks.
  Every write is carried out on both disks
    Reads can take place from either disk
  If one disk in a pair fails, data still available in the other
    Data loss would occur only if a disk fails, and its mirror disk also fails before the system is repaired
      Probability of combined event is very small
        Except for dependent failure modes such as fire or building collapse or electrical power surges
Mean time to data loss depends on mean time to failure, and mean time to repair
  E.g., MTTF of 100,000 hours, mean time to repair of 10 hours gives mean time to data loss of 500*106 hours (or 57,000 years) for a mirrored pair of disks (ignoring dependent failure modes)

## Slide 23: Improvement in Performance via Parallelism
Two main goals of parallelism in a disk system:
  1. Load balance multiple small accesses to increase throughput
  2. Parallelize large accesses to reduce response time.
Improve transfer rate by striping data across multiple disks.
Bit-level striping – split the bits of each byte across multiple disks
  In an array of eight disks, write bit i of each byte to disk i.
  Each access can read data at eight times the rate of a single disk.
  But seek/access time worse than for a single disk
    Bit level striping is not used much any more
Block-level striping – with n disks, block i of a file goes to disk (i mod n) + 1
  Requests for different blocks can run in parallel if the blocks reside on different disks
  A request for a long sequence of blocks can utilize all disks in parallel

## Slide 24: RAID Levels
Schemes to provide redundancy at lower cost by using disk striping combined with parity bits
  Different RAID organizations, or RAID levels, have differing cost, performance and reliability characteristics
RAID Level 0: Block striping; non-redundant.
  Used in high-performance applications where data loss is not critical.
RAID Level 1: Mirrored disks with block striping
  Offers best write performance.
  Popular for applications such as storing log files in a database system.

## Slide 25: RAID Levels (Cont.)
Parity blocks: Parity block j stores XOR of bits from block j of each disk
  When writing data to a block j, parity block j must also be computed and written to disk
    Can be done by using old parity block, old value of current block and new value of current block (2 block reads + 2 block writes)
    Or by recomputing the parity value using the new values of blocks corresponding to the parity block
      More efficient for writing large amounts of data sequentially
  To recover data for a block, compute XOR of bits from all other blocks in the set including the parity block

## Slide 26: RAID Levels (Cont.)
RAID Level 5: Block-Interleaved Distributed Parity; partitions data and parity among all N + 1 disks, rather than storing data in N disks and parity in 1 disk.
  E.g., with 5 disks, parity block for nth set of blocks is stored on disk (n mod 5) + 1, with the data blocks stored on the other 4 disks
  Block writes occur in parallel if the blocks and their parity blocks are on different disks

## Slide 27: RAID Levels (Cont.)
RAID Level 6: P+Q Redundancy scheme; similar to Level 5, but stores two error correction blocks (P, Q) instead of single parity block to guard against multiple disk failures.
  Better reliability than Level 5 at a higher cost
    Becoming more important as storage sizes increase

## Slide 28: RAID Levels (Cont.)
Other levels (not used in practice):
  RAID Level 2: Memory-Style Error-Correcting-Codes (ECC) with bit striping.
  RAID Level 3: Bit-Interleaved Parity
  RAID Level 4: Block-Interleaved Parity; uses block-level striping, and keeps a parity block on a separate parity disk for corresponding blocks from N other disks.
    RAID 5 is better than RAID 4, since with RAID 4 with random writes, parity disk gets much higher write load than other disks and becomes a bottleneck

## Slide 29
LSI MegaRAID SAS 8708EM2 ￥2000
RAID卡：
  实现RAID功能的板卡，由I/O处理器、硬盘控制器、硬盘连接器和缓存等构成
  将多个磁盘/固态硬盘驱动器在逻辑上组织为一个磁盘驱动器，管理多个磁盘驱动器同时传输数据
高档主板可实现RAID功能
RAID卡

## Slide 30: Choice of RAID Level
Factors in choosing RAID level
  Monetary cost
  Performance: Number of I/O operations per second, and bandwidth during normal operation
  Performance during failure
  Performance during rebuild of failed disk
    Including time taken to rebuild failed disk
RAID 0 is used only when data safety is not important
  E.g., data can be recovered quickly from other sources

## Slide 31: Choice of RAID Level (Cont.)
Level 1 provides much better write performance than level 5
  Level 5 requires at least 2 block reads and 2 block writes to write a single block, whereas Level 1 only requires 2 block writes
Level 1 had higher storage cost than level 5
Level 5 is preferred for applications where writes are sequential and large (many blocks), and need large amounts of data storage
RAID 1 is preferred for applications with many random/small updates
Level 6 gives better data protection than RAID 5 since it can tolerate two disk (or disk block) failures
  Increasing in importance since latent block failures on one disk, coupled with a failure of another disk can result in data loss with RAID 1 and RAID 5.

## Slide 32: 12.6 Disk-Block Access
Buffering: in-memory buffer to cache disk blocks
Read-ahead: Read extra blocks from a track in anticipation that they will be requested soon
Disk-arm-scheduling algorithms re-order block requests so that disk arm movement is minimized
  elevator algorithm

## Slide 33: Optimization of Disk Block Access (Cont.)
File organization
  Allocate blocks of a file in as contiguous a manner as possible
  Allocation in units of extents
  Files may get fragmented
    E.g., if free blocks on disk are scattered, and newly created file has its blocks scattered over the disk
    Sequential access to a fragmented file results in increased disk arm movement
    Some systems have utilities to defragment the file system, in order to speed up file access
Non-volatile write buffers

## Slide 34: Thanks for your attention